## Slide 1: Towards Multi-Permeability Cores Through Composition-Controlled Pellet Extrusion
Student Seminar

## Slide 2: Agenda
Who am I?
Introduction to additive manufacturing (AM)
Constant flux inductor (CFI)
Multi-permeability magnetic cores
Current field of 3D printing magnetics
Outlined research direction
Research questions

## Slide 3: Who am I?
Artis Fils
Experience:
BSc in Mechatronics from University of Southern Denmark (SDU)
MSc in Mechatronics from University of Southern Denmark (SDU)
Additive Manufacturing student worker for 4.5 years
Interests:
Additive manufacturing
3D printed electronics
Hybrid manufacturing
Currently:
Research assistant focusing on 3D printing magnetics since 1st of October 2026.

## Slide 4: What is additive manufacturing?

## Slide 5: 3D printing vs additive manufacturing
Model
Slice
Print

## Slide 6: Why additive manufacturing?
Advantages
Fast design iterations
Complex geometries
Multi material capabilities
Disadvantages
Slow manufacturing
Resolution & surface finish
Feedstock limitations

## Slide 7: Advantage – Fast Design iterations

## Slide 8: Advantage – Complex geometries

## Slide 9: Advantages – Multi-material capabilities

## Slide 10: Disadvantage – Slow manufacturing

## Slide 11: Disadvantage – Resolution & surface finish

## Slide 12: Disadvantage – Feedstock limitations

## Slide 13: Most common methods of additive manufacturing

## Slide 14: What is Fused Deposition Modeling (FDM)?

## Slide 15: Constant-flux inductor (CFI)
A constant-flux inductor is an magnetic component designed to distribute magnetic flux uniformly across its core.

## Slide 16: Constant-flux inductor (CFI)
A constant-flux inductor is an magnetic component designed to distribute magnetic flux uniformly across its core.
Benefits:
Prevents localized saturation
Distributes the temperature
Reduces the footprint

## Slide 17: Constant-flux inductor (CFI)
A constant-flux inductor is an magnetic component designed to distribute magnetic flux uniformly across its core.
Benefits:
Prevents localized saturation
Distributes the temperature
Reduces the footprint
Tradeoff:
Manufacturing complexity
Cost
Physical tuning

## Slide 18: Methods of designing a CFI
Specialized geometry
Multi-permeability

## Slide 19: Methods of designing a CFI
Specialized geometry
Multi-permeability

## Slide 20: Methods of designing a CFI
Specialized geometry
Multi-permeability

## Slide 21: Methods of designing a CFI
Geometry and permeability are not mutually exclusive design variables, and optimizing both may offer further benefits.
Custom and complex -> perfectly suited for AM.
Specialized geometry
Multi-permeability

## Slide 22: Current field of 3D printing magnetics
3D printing magnetics
Vat polymerization
Powder bed fusion
Binder jetting
Material extrusion
Fused deposition modeling
Direct ink writing
Fused granulate fabrication

## Slide 23: Current field of 3D printing magnetics
3D printing magnetics
Vat polymerization
Powder bed fusion
Binder jetting
Material extrusion
Fused deposition modeling
Direct ink writing
Fused granulate fabrication

## Slide 24: FDM vs FGF vs DIW
Fused Deposition Modeling (FDM)
Fused Granulate Fabrication (FGF)
Direct Ink Writing (DIW)

## Slide 25: FDM vs FGF vs DIW
Fused Deposition Modeling (FDM)
Fused Granulate Fabrication (FGF)
Direct Ink Writing (DIW)
Low
Process complexity
High
Permeability

## Slide 26: Research direction
Fused Granulate Fabrication (FGF)
Multi-permeability cores

## Slide 27: Multi-permeability via different materials
PA12 with x wt% FeSiAl (μrx)
PA12 with y wt% FeSiAl (μry)
PA12 with z wt% FeSiAl (μrz)

## Slide 28: Multi-permeability via different materials
PA12 with x wt% FeSiAl (μrx)
PA12 with y wt% FeSiAl (μry)
PA12 with z wt% FeSiAl (μrz)

## Slide 29: Multi-permeability via mixing different ratios
PA12 with 86 wt% FeSiAl (μr_100:0)
PA12

## Slide 30: Multi-permeability via mixing different ratios
μr_25:75
μr_75:25
PA12 with 86 wt% FeSiAl (μr_100:0)
PA12

## Slide 31: Research questions
Can varying the blend ratio of magnetic-filled and unfilled polymer pellets produce reproducible changes in the permeability of a soft-magnetic composite manufactured using a commercial pellet extruder?
μr_25:75_1 = μr_25:75_2 ?
μr_75:25_1 = μr_75:25_2 ?

## Slide 32: Research questions
Can varying the blend ratio of magnetic-filled and unfilled polymer pellets produce reproducible changes in the permeability of a soft-magnetic composite manufactured using a commercial pellet extruder?
Process
Filler amount
Filler uniformity
Permeability
Specimen
Correlation?

## Slide 33: Research questions
Can discrete permeability regions be fabricated by sequentially printing pre-blended pellet batches, using controlled purging to achieve distinct and reproducible material compositions?

## Slide 34: Research questions
Can discrete permeability regions be fabricated by sequentially printing pre-blended pellet batches, using controlled purging to achieve distinct and reproducible material compositions?
Purging
Single-permeability specimen
Inductance
Saturation behaviour
Core loss
Multi-permeability specimen
Inductance
Saturation behaviour
Core loss
Comparisson

## Slide 35: Summary
Constant flux inductors (CFI) are beneficial with a complexity tradeoff.
Multi-permeability cores are an approach to produce CFI.
Additive manufacturing (AM) provides multi-material and complex geometry capabilities.
AM methods have been used to manufacture CFIs.
Fused Granulate Fabrication (FGF) strikes as a balanced approach in material extrusion.
Whether FGF can be used to manufacture multi-permeability cores is unanswered.

## Slide 36: Contacts
Office – Building 325, Room 222
Email – artfi@dtu.dk
LinkedIn – Artis Fils
ORCID – Artis Fils